## Slide 1: A Tool for Estimating Impervious Surface Growth of Development Scenarios
Kevin Ramsey, Ph.D.
U.S. EPA Office of Sustainable Communities
202.566.1153
Ramsey.Kevin@epa.gov

## Slide 2: The Problem
We know that…
  Infill development results in less new impervious surface area than does greenfield development
However…
  Existing methods for quantifying the impervious surface impacts of alternative development scenarios are either…
    Expensive , time-consuming, and/or data-hungry
    Overly simplified and insensitive to location

## Slide 3: The Need
A tool that is…
Simple, easy to use
Has no data requirements
Accounts for location characteristics
Accounts for impervious surface growth on the development site as well as immediate surrounding area (e.g., roads)

## Slide 4: EPA’s Impervious Surface Growth Model (ISGM) Tool: Key Characteristics
Estimates acres of impervious surface growth per new housing unit or employee as a function of:
  Housing density (housing units per unprotected acre)
  Employment density (employees per unprotected acre)
  Regional accessibility (jobs within 30 miles, dist. weighted)
Tool is pre-loaded with density and accessibility data for all census block groups in the U.S.

## Slide 5: The Model

## Slide 6: ISGM Interface

## Slide 7: How to determine a location’s CBG ID (for those who aren’t GIS experts)
A Census Block Group (CBG) is a unit of census geography. Each CBG has a 12-digit unique identifier. We call it “CBG ID”.
Eventually we’d love for this tool to automatically geocode street addresses. In the meantime, here is an easy solution for identifying the CBG ID of a single location of interest:
  Go to: http://bit.ly/wLxawB
  Type a street address into the search box. Map will zoom to location.
  Click on the map near the location. An info box will appear. At the top is the block group id. Copy it.
  Right click in an empty cell of the CBG ID column of the ISGM tool and select “Paste special”. Choose “text”.
  Edit the pasted text to remove the period in the id number.

## Slide 8: Example Location 1: Infill near Potomac Metro
100 new housing units
25 new jobs
0.5 Acres new impervious surface

## Slide 9: Example Location 2: Glenmont, MD
100 new housing units
25 new jobs
4.1 Acres new impervious surface

## Slide 10: Example Location 3: Greenfield in Ashton, MD
100 new housing units
25 new jobs
8.1 Acres new impervious surface

## Slide 11: Net impervious surface growth (in acres) from adding 100 housing units and 25 jobs
Chart: 
| Potomic Ave, DC | Glenmont, MD | Ashton, MD
 | 0.4869 | 4.0991 | 8.133

## Slide 12: What is Not Accounted for in the ISGM
Impervious surface area at site prior to development
Urban design (e.g., street and sidewalk width)
Type of commercial activity
Impervious surface expansion outside of the immediate block group (e.g., expansion of arterials leading to a new development)
Policies and zoning that would affect the form/density of new development
See report for detailed discussion of limitations.

## Slide 13: Potential Uses of this Tool/Model
OSC is working with others to evaluate the appropriateness of the ISGM/tool for supporting the following kinds of activities:
  Roughly comparing impervious surface impacts of alternative development scenarios
  Integrate with scenario planning tools for improved impervious surface indicators
  Integrate with water quality impact assessment tools

## Slide 14: Acknowledgements
Thanks to Aaron Poresky and Geosyntec Consultants for developing the impervious surface growth model and tool in collaboration with EPA’s Office of Sustainable Communities.